3GPP LI 	Tdoc S3LI01_073

Munich June 05-07

| CR-Form-v3 |
| --- |
| CHANGE REQUEST |
| ( | 33.107 | CR | xxx | ( rev | - | ( Current version: | 3.2.0 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | (U)SIM |  | ME/UE |  | Radio Access Network |  | Core Network | X |
| Title: ( | Reporting of Secondary PDP context |
| Source: ( | SA WG3 LI |
| Work item code: ( | Security |  | Date: ( | June 7, 2001 |
| Category: ( | A |  | Release: ( | REL-4 |
|  | Use one of the following categories: F (essential correction) A (corresponds to a correction in an earlier release) B (Addition of feature), C (Functional modification of feature) D (Editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: 2 (GSM Phase 2) R96 (Release 1996) R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) REL-4 (Release 4) REL-5 (Release 5) |
| Reason for change: ( | Ambiguity related to reporting of secondary PDP context |
| Summary of change: ( | Clarify that secondary PDP context is to be reported. |
| Consequences if ( not approved: | Ambiguity remains |
| Clauses affected: ( | 7.4.3 and 7.4.5 |
| Other specs ( |  | Other core specifications ( |  |
| affected: |  | Test specifications |  |
|  |  | O&M Specifications |  |
| Other comments: ( |  |

How to create CRs using this form:

Comprehensive information and tips about how to create CRs can be found at: http://www.3gpp.org/3G_Specs/CRs.htm.  Below is a brief summary:

1)	Fill out the above form. The symbols above marked ( contain pop-up help information about the field that they are closest to.

2)	Obtain the latest version for the release of the specification to which the change is proposed. Use the MS Word "revision marks"  feature (also known as "track changes") when making the changes. All 3GPP specifications can be downloaded from the 3GPP server under ftp://www.3gpp.org/specs/ For the latest version, look for the directory name with the latest date e.g. 2000-09 contains the specifications resulting from the September 2000 TSG meetings.

3)	With "track changes" disabled, paste the entire CR form (use CTRL-A to select it) into the specification just in front of the clause containing the first piece of changed text.  Delete those parts of the specification which are not relevant to the change request.

****    FIRST MODIFIED SECTION    ****

### 7.4.3	Packet Data PDP context activation

For primary PDP context activation and for secondary PDP context activation a PDP context activation-event is generated. When a PDP context activation is generated from the mobile to 3G GSN this event is generated. These fields will be delivered to the DF2 if available:

Observed MSISDN

Observed IMSI

Observed IMEI

PDP address of observed party

Event Type

Event Time

Event Date

Correlation number

Access Point Name

PDP Type

Network Element Identifier

Location Information

Failed context activation reason

IAs (if applicable)

NOTE: Each primary and secondary PDP context must use a unique Correlation number.

****    SECOND MODIFIED SECTION    ****

### 7.4.5	Packet Data PDP context deactivation

At deactivation of a primary PDP context and at deactivation of a secondary PDP context a PDP context deactivation-event is generated. These fields will be delivered to the DF2if available:

Observed MSISDN

Observed IMSI

Observed IMEI

PDP address of observed party

Event Type

Event Time

Event Date

Correlation number

Access point name

Network Element Identifier

Location Information

IAs (if applicable)

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to http://www.3gpp.org/3G_Specs/3G_Specs.htm

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or several companies or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. Work item acronyms are listed in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "3GPP working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. essential correction).

Enter each the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

This is an example of pop-up text.