3GPP LI 	Tdoc S3LI02_002

Amsterdam January 29-31, 2001

| CR-Form-v3 |
| --- |
| CHANGE REQUEST |
| ( | 33.107 | CR | Xxx | ( rev | - | ( Current version: | 5.00 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | (U)SIM |  | ME/UE |  | Radio Access Network |  | Core Network | X |
| Title: ( | Addition of PDP context modification Event |
| Source: ( | MvJ |
| Work item code: ( | Security |  | Date: ( | 21 November 2001 |
| Category: ( | B |  | Release: ( | REL-5 |
|  | Use one of the following categories: F (essential correction) A (corresponds to a correction in an earlier release) B (Addition of feature), C (Functional modification of feature) D (Editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: 2 (GSM Phase 2) R96 (Release 1996) R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) REL-4 (Release 4) REL-5 (Release 5) |
| Reason for change: ( | The PDP context modification procedure is invoked by the network in order to change the QoS negotiated during the PDP context activation procedure or at previously performed PDP context modification procedures. The procedure can be initiated by the network at any time when a PDP context is active. Currently the specification does not support reporting of this procedure. Accordingly, the “PDP context modification” event is being added to the set of reported events. |
| Summary of change: ( | Reporting of the PDP Contect Modification event is being added to this specification . See also S3LI01_102 / 103 |
| Consequences if ( not approved: | Missing capability and compatibility with 3GPP TS 23.060. ?? |
| Clauses affected: ( | 7.3.2, 7.4.8 |
| Other specs ( |  | Other core specifications ( |  |
| Affected: |  | Test specifications |  |
|  |  | O&M Specifications |  |
| Other comments: ( |  |

How to create CRs using this form:

Comprehensive information and tips about how to create CRs can be found at: http://www.3gpp.org/3G_Specs/CRs.htm.  Below is a brief summary:

1)	Fill out the above form. The symbols above marked ( contain pop-up help information about the field that they are closest to.

2)	Obtain the latest version for the release of the specification to which the change is proposed. Use the MS Word "revision marks"  feature (also known as "track changes") when making the changes. All 3GPP specifications can be downloaded from the 3GPP server under ftp://www.3gpp.org/specs/ For the latest version, look for the directory name with the latest date e.g. 2000-09 contains the specifications resulting from the September 2000 TSG meetings.

3)	With "track changes" disabled, paste the entire CR form (use CTRL-A to select it) into the specification just in front of the clause containing the first piece of changed text.  Delete those parts of the specification which are not relevant to the change request.

### 7.3.2	Structure of the events

There are seven different events in which the information is sent to the DF2 if this is required. Details are described in the following section. The events for interception are configurable (if they are sent to DF2) in the 3G GSN and can be suppressed in the DF2.

The following events are applicable to 3G SGSN:

-	Mobile Station Attach;

-	Mobile Station Detach;

-	PDP context activation;

-	Start of intercept with PDP context active;

-	PDP context modification

-	PDP context deactivation;

-	RA update;

-	SMS.

NOTE:	3G GGSN interception is a national option. Location information may not be available in this case.

The following events are applicable to the 3G GGSN:

-	PDP context activation ;

-	PDP context modification

-	PDP context deactivation ;

-	Start of interception with PDP context active.

A set of fields as shown below is used to generate the events. The events transmit the information from 3G GSN to DF2. This set of fields as shown below can be extended in the 3G GSN, if this is necessary as a national option. DF2 can extend this information if this is necessary as a national option e.g. a unique number for each surveillance warrant.

Table 2: Information Events for Packet Data Event Records

Observed MSISDN MSISDN of the target subscriber (monitored subscriber)

Observed IMSI IMSI of the target subscriber (monitored subscriber)

Observed IMEI IMEI of the target subscriber (monitored subscriber),it shall be checked for each activation over the radio interface.

Event type Description which type of event is delivered: MS attach, MS detach, PDP context activation, Start of intercept with PDP context active, PDP context deactivation, SMS, Cell and/or RA update,

Event date Date of the event generation in the 3G GSN

Event time Time of the event generation in the 3G GSN

PDP address The PDP address of the target subscriber. Note that this address might be dynamic.

Access Point Name The APN of the access point. (Typically the GGSN of the other party)

Location Information Location Information is the service area identity, RAI and/or location area identity that is present at the GSN at the time of event record production.

PDP Type The used PDP type.

Correlation Number The correlation number is used to correlate CC and IRI.

SMS The SMS content with header which is sent with the SMS-service. The header also includes the SMS-Centre address.

Network Element IdentifierUnique identifier for the element reporting the ICE.

Failed attach reason Reason for failed attach of the target subscriber.

Failed context activation reason Reason for failed context activation of the target subscriber.

IAs The observed Interception Areas

Request Initiator The initiator of the PDP context activation, deactivation or modification request either the network or the 3G MS.

QoS This field indicates the Quality of Service associated with the PDP Context procedure.

### 7.4.8	Packet Data PDP context modification

This event will be generated if interception for a target is started and if the target has at least one PDP context active. These fields will be delivered to the DF2 if available:

Observed MSISDN

Observed IMSI

Observed IMEI

PDP address of observed party

Event Type

Event Time

Event Date

Correlation number

Access Point Name

PDP Type

Network Element Identifier

Location Information

IAs (if applicable)

Request Initiator

QoS

# Comments

Page: 1
 Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Page: 1
 Enter the CR number here. This number is allocated by the 3GPP support team.

Page: 1
 Enter the revision number of the CR here. If it is the first version, use a "-".

Page: 1
 Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to http://www.3gpp.org/3G_Specs/3G_Specs.htm

Page: 1
 For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Page: 1
 Mark one or more of the boxes with an X.

Page: 1
 Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Page: 1
 Enter the source of the CR. This is either (a) one or several companies or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

Page: 1
 Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. Work item acronyms are listed in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/

Page: 1
 Enter the date on which the CR was last revised.

Page: 1
 Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "3GPP working methods".

Page: 1
 Enter a single release code from the list below.

Page: 1
 Enter text which explains why the change is necessary.

Page: 1
 Enter text which describes the most important components of the change. i.e. How the change is made.

Page: 1
 Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. essential correction).

Page: 1
 Enter each the number of each clause which contains changes.

Page: 1
 Enter an X in the box if any other specifications are affected by this change.

Page: 1
 List here the specifications which are affected or the CRs which are linked.

Page: 1
 Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

Page: 1
 This is an example of pop-up text.